## Slide 1: LANDFILL SOLUTIONS
  Within the filtration and separation sector, our company offers solutions and equipment for landfills. In cooperation with the Swiss company Hofstetter AG, we offer solutions for landfill gas, leachate and odor control.

## Slide 2: LANDFILL SOLUTIONS

## Slide 3: LANDFILL GAS SYSTEMS
Our standard modular gas plants are the ideal solution for landfill gas with a methane concentration of 5 - 55%. The basic module includes a moisture removal system, a blower, a torch and a fully automatic PLC control system. For older landfills where waste is no longer deposited, we designed the LOWCAL flare, which has the ability to burn landfill gas with a methane concentration of up to 15%.
Gas flow 20-6,000 Nm3/h
Thermal capacity 100-45,000 kW
Combustion temperature 800-1,200 °C

## Slide 5: LEACHETE FILTRATION SYSTEMS
Landfill leachates are among the most harmful waste waters. A large amount of salt, heavy metals and non-biodegradable contents cannot be treated with conventional wastewater treatment, but requires special treatment. HOFSTETTER meets this challenge by using standard spiral membranes as well as advanced DT modules for reverse osmosis. In just one step, the modules remove a full range of contaminants including bacteria, viruses and suspended solids. The unique design of the module ensures easy cleaning and reduces the risk of clogging. Individual modules can be easily opened for review purposes. The membranes, as well as the complete plant, are always adapted to the specific conditions of the client.
1-25 m3/hour per line
Efficiency up to 95%
Working pressure up to 160 bar

## Slide 7: AUTONOMUS OFFGRID SYSTEMS
Fully autonomous all-in-one container-type offgrid plants that contain:
Landfill gas collection and filtration;
Generator for electricity production;
Torch;
Leachete filtration system.
This kind of system can be installed in landfills outside the populated area, where there is no access to the infrastructure network.

## Slide 8: TURNKEY SOLUTIONS
In addition to the plant, we offer turnkey services, consisting of the following processes:
Research and optimization of landfills;
Theoretical forecasts of gas production, test pumping;
Designing a gas collection system;
Designing a system to reduce unpleasant odors;
Security checks;
Training Commissioning Delivery of spare parts ;
Consulting, assessments and due diligence.